X-RAAS
1.0
X-RAAS implements a simulation of the Honeywell Runway Awareness and Advisory System (RAAS), which is itself an extension to the Enhanced Ground Proximity Warning System (EGPWS) software. RAAS operates by monitoring aircraft position and various sensor inputs and issues advisory and warning aural and visual annunciations to warn the flight crew of potential hazards to the aircraft. X-RAAS models most of the aural annunciations. Modeling visual annunciations would require integration with 3rd party aircraft add-ons, which was at this time not a primary consideration.
Installation
X-RAAS is written in Lua and as such requires the FlyWithLua plugin for X-Plane. Once that is installed, to install X-RAAS into FlyWithLua, simply copy all the files provided in the compressed ZIP file to the <X-Plane 10>/Resources/plugins/FlyWithLua/Scripts folder. X-RAAS is for the most part fully automated, but you are encouraged to read through this manual to fully understand what it monitors and how to extract the most use from its advisories.

Activating X-RAAS in the aircraft
X-RAAS automatically begins functioning as soon as electrical power is applied to the aircraft's primary avionics systems. Normally, RAAS is only used for airliner operations and its advisories and performance monitoring can be a poor fit for small general aviation aircraft or aircraft with performance significantly different from airliners (such as helicopters). To avert this, by default X-RAAS checks two parameters about the currently loaded aircraft prior to starting up:
- The aircraft must have at least two or more engines.
- The aircraft's Maximum Take Off Weight (MTOW) must be at least 5,700 kg or more.
If any of these parameters is below the above mentioned limits, X-RAAS startup is inhibited. Both of these limits are configurable in the X-RAAS configuration file, so it is possible to re-enable X-RAAS for any aircraft in X-Plane, provided sufficient electrical power is available. See below for details on how to fine tune X-RAAS's behavior.
# X-RAAS Electrical System Integration
X-RAAS is internally connected to electrical bus #1 and #2 in the aircraft (normally the “left” and “right” electrical bus) and is also subject to the master “Avionics on” switch (if installed on the aircraft). Losing power on both electrical buses or setting the master avionics switch to the “off” position will result in X-RAAS shutting down. X-RAAS requires a minimum of at least 11 Volts to be present on one of the electrical buses to operate and nominally consumes around 40 Watts of power. To prevent generating an additional electrical load by a non-flight-critical advisory system when the aircraft is operating only on battery electrical power, X-RAAS monitors if at least one engine generator or the APU generator is connected to the electrical buses and will automatically shut down if the aircraft is only operating on battery or external power (during external power operation the aircraft can be safely assumed to be on the ground and stationary).
X-RAAS Advisories
# Approaching a runway on the ground
X-RAAS constructs a virtual bounding box around each runway which extends laterally approximately 1.5x the runway width from the runway centerline and 1500 feet longitudinally from each runway threshold. X-RAAS will issue an advisory in case the aircraft's nose is approximately 1 second from penetrating this bounding box (calculated based on ground speed):

Illustration 1: Approaching a runway on the ground
The advisory is inhibited when ground speed exceeds 40 knots (to prevent activation on takeoff through intersecting runways). Please also note that the annunciation does not guarantee the ability to stop before entering the runway.
# Lined up on runway for takeoff
Illustration 2: Lined up on runway for takeoff
This annunciation is made on initially lining up on a runway (aircraft heading is within approximately 20 degrees of runway heading). If the aircraft holds in position on a runway for extended periods of time, the annunciation is repeated at configurable intervals up to a configurable maximum number of repetitions before auto-inhibiting.
This annunciation may be supplemented by an annunciation of “FLAPS, FLAPS” if the appropriate takeoff flap configuration has not yet been selected at the time of line up. This is to prevent the activation of the takeoff configuration horn (as that would necessitate a takeoff abort).
# Lined up on runway too short for takeoff
Illustration 3: Lined up on runway too short takeoff
If the runway length remaining for takeoff is below an operator-defined minimum for a safe takeoff, the “on runway” annunciation is supplemented a by runway distance remaining readout.

# Short runway takeoff
If a takeoff is attempted on a runway with runway length remaining below an operator defined minimum, once ground speed exceeds 40 knots, a warning annunciation is generated: “CAUTION! SHORT RUNWAY! SHORT RUNWAY!”
Illustration 4: Short runway takeoff

# Taxiway takeoff
This annunciation warns of attempting takeoff on a taxiway, typically after missing a 90 degree (or greater) turn onto a runway.
Illustration 5: Taxiway takeoff
The conditions for triggering this annunciation are:
- Aircraft is NOT on a runway
- Ground speed exceeds 40 knots

# Altimeter setting climbing through transition altitude
X-RAAS determines the transition altitude based on navigational database entries based on the nearest airport to the aircraft. If the aircraft climbs through the transition altitude, X-RAAS monitors the barometric altimeter subscale setting and if by 30 seconds after transitioning the subscale is not set to QNE (1013.25 hPa or 29.92 in.Hg) it issues the following advisory: “ALTIMETER SETTING”. This is to prevent incorrect altitude readings in cruise, which increases the possibility of traffic collisions.

Illustration 6: Altimeter setting climbing through transition altitude
Please note that this advisory might not be available if transition altitude is not published in the navigation database. Flight crews must remain fully alert to crossing the transition altitude and reliance on the altimeter setting RAAS annunciation as part of standard operations is prohibited.
# Altimeter setting descending through transition level
This is the reverse advisory to the altimeter setting advisory during climb and is intended to assist in preventing CFIT (Controlled Flight Into Terrain). X-RAAS determines the transition level based on the navigational database entries of the airport closest to the aircraft. If a fixed transition level is not published, X-RAAS calculates the lowest possible transition level based on barometric pressure readings, GPS calculated elevation AMSL and a published transition altitude, such that the calculated transition level is equal in true elevation AMSL to the transition altitude. Please note that this fallback mechanism might not be as accurate as using the ATC-assigned transition level, so reliance on this annunciation to determine the correct transition level is prohibited.
Once the aircraft descends through the transition level, X-RAAS monitors the barometric altimeter reading and GPS-calculated elevation MSL. If they differ by more than a pre-determined threshold after more than 30 seconds has elapsed since crossing the transition level, an “ALTIMETER SETTING” annunciation is generated. This 30 second timeout can be preempted and the altimeter setting check initiated early if the aircraft descends below 1,500 feet above field elevation of the nearest airport. To support operation with QFE altimetry, X-RAAS also allows an altimeter setting which yields an altitude reading which reads close to above field elevation of the closest airport.

Illustration 7: Altimeter setting descending through transition level
# Approaching a runway to landing
To facilitate proper runway alignment, X-RAAS issues a runway approach annunciation also when approaching a runway from the air with the intention to land. The following conditions need to be met for this annunciation:
- Within approximately 3 nm of a runway.
- Track is aligned with the runway and heading is within 20 degrees of runway heading.
- In landing configuration.
- Descending through between 470 feet and 220 feet above runway threshold elevation.
If the runway length is below an operator-defined minimum, the annunciation is supplemented by an additional callout: “CAUTION! SHORT RUNWAY! SHORT RUNWAY!”

Illustration 8: Approaching a runway to landing
# Late flap selection during approach to land
X-RAAS also monitors the flaps configuration during an approach to land and issues “FLAPS! FLAPS!” advisories in case flaps are not in the proper setting for landing at certain periods during the approach, depending elevation above runway threshold:
- Descending through 950 feet to 700 feet, annunciation: “FLAPS! FLAPS!”
- Descending through 600 feet to 470 feet, annunciation: “FLAPS! FLAPS!”
- Descending through 470 feet to 220 feet, annunciation: “UNSTABLE! UNSTABLE!”
- Annunciation is inhibited below 220 feet above threshold elevation.

Illustration 9: Late flap selection during approach to land
# Steep descent late in the approach to land
To protect against steep descents late in the landing approach and “dive bombing it” at the last moment, X-RAAS calculates the aircraft glide path angle and compares it with the optimal glide path angle stored in the database for the runway. If the actual glide path angle exceeds 1.5x the optimal angle (but no more than 8 degrees absolute glide path angle), X-RAAS issues advisories, depending elevation above runway threshold:
- Descending through 950 feet to 700 feet, annunciation: “TOO HIGH! TOO HIGH!”
- Descending through 600 feet to 470 feet, annunciation: “TOO HIGH! TOO HIGH!”
- Descending through 470 feet to 220 feet, annunciation: “UNSTABLE! UNSTABLE!”
- Annunciation is inhibited below 220 feet above threshold elevation.

Illustration 10: Steep descent late in the approach to land
# Landing rollout runway length remaining
The landing rollout annunciations inform the crew of remaining distance for landing rollout. They are initiated as soon the aircraft reaches 5 feet radio altitude and remain in effect until the ground speed is below 40 knots (except for the last 100 feet / 30 meters annunciation, which is sounded irrespective of ground speed as long as the aircraft remains aligned with the runway).
The annunciations are suppressed during go-around (radio altitude below 100 feet and rate of climb 450 feet per minute or greater).
Landing distance remaining readouts are performed at 1000 foot / 300 meter increments and are based on the position the aircraft's nosewheel will attain in approximately 1 second with an added approximate 400 feet / 120 meter buffer (thus a “3000 (feet) remaining” annunciation can be sounded between 3000 to 3400 feet remaining). Initial landing distance remaining annunciations are commenced at 3000 feet / 2700 meters remaining, or an operator-defined maximum.

Illustration 11: Landing rollout runway length remaining
Due to the implementation, landing rollout annunciations are only guaranteed to sound if the aircraft is flying through each distance “gate” below a certain limiting ground speed.
Distance [feet]	Distance [meters]	Limiting ground speed [knots]
9000 – 1000	2700 – 300	235
500	100	118
100	30	59

# Long landing
This annunciation protects against excessive floating on landing or an incorrectly executed too high/too fast approach, resulting in touch down very far down the runway and potentially insufficient runway length available for rollout. Conditions for this annunciation are:
- The aircraft is above the runway.
- Radio altitude indicates less than 50 feet, but more than 5 feet.
- Aircraft is past ½ of the runway length or remaining runway length is less than an operator-specified minimum.

Illustration 12: Long landing
X-RAAS will initially annunciate “LONG LANDING!” twice and the remaining runway length if it is less than 9000 feet (2700 meters). Afterwards, X-RAAS will continue to annunciate runway length remaining every 1000 feet (300 meters), unless the aircraft lands and decelerates below 40 knots ground speed, or performs a go-around (refer to the previous section for conditions monitored during a go-around).